## Slide 1
Simulation of large network:
Generate vehicle locations and road angles from data
Investigate a dense and a sparse network
Compared three approaches: (1) centralized, (2) decentralized with optimized fusion weights,
(3) decentralized with random fusion weights
Findings:
For dense network: no statistically significant difference
For sparse network: (1) better than (2) better than (3), significantly.

## Slide 2
Network connection plot
The dense network

## Slide 3
 | Centralized | Optimized | Random
RMSE (m) | 0.67 | 0.76 | 0.72
*Random: randomly select numbers of particle to be fused, and make sure the total transmitted
numbers equal approximately to the optimized case (same communication bandwidth)

## Slide 4
 | Centralized | Optimized | Random
RMSE (m) | 0.67 | 0.94 | 1.64
Noted from the error plot: RMSE Root of variance, approximately.
The sparsest network

## Slide 5
 | Centralized | Optimized | Random
RMSE (m) | 0.67 | 1.02 | 0.98
With medium sparcity